## Slide 1
How Do People Edit Light Fields?
Adrian Jarabo1* Belen Masia1* Adrien Bousseau2 Fabio Pellacini3 Diego Gutierrez1
1Universidad de Zaragoza 2Inria 3Sapienza Università di Roma

## Slide 2: A ‘new kind’ of pictures
A ‘new kind’ of pictures
Notes: Light fields, in addition to their benefits in IBR, have brought with them a new kind of pictures.
------------------------------------------
Nr of papers in sigg
Nr of companies selling LF cams – Lytro/Raytrix sales?
Adobe?
Examples of unstructured?
http://www.theverge.com/2014/1/7/5285162/sharps-massive-85-inch-8k-3dtv-concept-is-far-from-ready-for-prime-time
http://www.engadget.com/2014/01/08/sharp-85-inch-8k-3d-tv/

## Slide 3
A ‘new kind’ of pictures
Notes: Among the features of this new kind of pictures, one of them is shifting the point of view, as you see here.
(Here you see a small shifting, but actually, how much you can shift it depends on your baseline during capture.)

## Slide 4: Not just view shifting…
Focus shifting
Source: LightField Forum
Notes: But light fields are not only about view shifting.
You can also shift and adjust the focus post-capture, as shown here, obtaining different artistic and semantic effects on the same scene.

## Slide 5: Not just view shifting…
Stereo content creation
Source: LightField Forum
Notes: Or you can generate stereo pairs from a light field
(and, interestingly, not necessarily with a single center of projection, as has been shown by previous work).

## Slide 6
Scene reconstruction
Not just view shifting…
[Kim et al. 2013]
Notes: As yet another application of light fields, they are being used, with very promising results, for dense scene reconstruction
(, like the one shown here by Kim et al.)
(This provides valuable information from the scene, allowing for a great number of editing operations, and facilitating scene understanding, material acquisition, etc.)

## Slide 7
85-inch 8K autostereoscopic TV by Sharp
Not just view shifting…
Content for glasses-free 3D displays
Notes: Further, light fields are the input to glasses-free 3D displays.
These displays still have a long way to go, but they are emerging, and manufacturers continue to display new prototypes every year, such as the one by Sharp shown here, with 8k in spatial resolution.
Actually, the fact that these displays require light fields as an input currently poses a major stumbling block in terms of content generation for them.
--------------------------------------------------------------------
http://www.theverge.com/2014/1/7/5285162/sharps-massive-85-inch-8k-3dtv-concept-is-far-from-ready-for-prime-time
http://www.engadget.com/2014/01/08/sharp-85-inch-8k-3d-tv/

## Slide 8
[Pamplona et al. 2012]
and for
tailored displays
Not just view shifting…
Content for glasses-free 3D displays
Input
image
Regular
display
Tailored
display
Notes: And light fields are also the input to a kind of displays
which have appeared in recent years that can compensate for visual aberrations.

## Slide 9: Light Fields
Image-based rendering
A new scene representation
  Advanced image editing
  Scene reconstruction
  View shifting
  All-in-focus
  Focus shifting
  Stereo content creation
  …
Notes: Light fields were conceived as a really powerful tool for image based rendering
But they have evolved and this new scene representation currently has numerous other applications like the ones we’ve just seen.

## Slide 10: Light field cameras proliferate…
RaytrixTM
LytroTM
Pelican Imaging
Pixar
Toshiba
[Raskar et al. 2007]
Adobe
Cafadis
Notes: As a result of this potential, light field cameras have already reached the consumer market.
Raytrix and Lytro have been the first to commercialize light field cameras in the mass market, Raytrix targeting industrial customers and Lytro targeting the wide public.
But many others including Adobe or Pixar have their own prototypes and patents.

## Slide 11
There is an increasing need for editing this new content
Notes: So it is clear that there is an increasing interest on light fields and their applications, with more devices for both capture and display.
As a result, we will need techniques, algorithms, software programs, that can edit this type of content.
However, very little is known or has been developed on how to manipulate and or modify the 4-dimensional structure that a light field is.

## Slide 12
A 4D structure
Notes: A light field is a four-dimensional representation of a scene, which we can see as a scene captured from different viewpoints,
During light field capture, we are effectively avoiding the angular integration that a conventional camera performs and thus capturing spatio-angular information, as in the light field shown here.

## Slide 13
2D
There is an increasing need for editing this new content
Notes: If we look at 2D conventional images, there is a huge body of work and sophisticated programs devoted to how to edit them.
For light fields, however, there is barely anything.

## Slide 14
→ 4D
?
2D
There is an increasing need for editing this new content
Notes: (So how do we edit this four-dimensional structure on a two-dimensional screen? )
This is what we are trying to address in this paper, how do we move around this 4D structure that a light field is.
Let me show you the challenge…

## Slide 15
2D
Notes: Say we have a 2D image we want to edit on our computer such as this image, and we want to paint a heart on the wall.
We can simply do it with any image editing software as simply as shown in this video.
However, if the image is not an image…

## Slide 16
4D
Unavailable
Inconvenient
Imperfect
Using depth
information?
It may be:
Notes: …but a light field, when we, for example, shift the viewpoint, the following can happen:
The edit is not placed correctly within the light field, and so it is not correctly propagated to all of its views.

## Slide 17
There is an increasing need for editing this new content
Our goal: Explore users’ preferences when navigating & editing a light field
Notes: Our goal is to find out what is the best way to edit a light field, which is a four dimensional structure, on a conventional two-dimensional screen that the majority of us has.
Let me note here that we are interested in editing workflows and not on specific editing tools.
Explore
How to move around this 4D space
Remove 2D screen
Entender esto antes de sacar 50k algoritmos de edición

## Slide 18
There is an increasing need for editing this new content
Our goal: Find out the preferred way to edit a 4D light field on a 2D screen
Notes: Our goal is to find out what is the best way to edit a light field, which is a four dimensional structure, on a conventional two-dimensional screen that the majority of us has.
Let me note here that we are interested in editing workflows and not on specific editing tools.
Explore
How to move around this 4D space
Remove 2D screen
Entender esto antes de sacar 50k algoritmos de edición

## Slide 19
(Distantly) Related Work
Morphing
Painting, scissoring
Pop-Up Light Field
Edit propagation
…
[Zhang et al. 2002]
[Seitz and Kutulakos 2002]
[Shum et al. 2004]
[Jarabo et al. 2011]
There is an increasing need for editing this new content
Notes: There is a number of previous works which have dealt with how to do specific editions with a light field, such as:
Morphing two light fields together
Or painting or cutting parts off a light field
Or PopUp Light Field, an interactive system in which the user divides the light field into a series of layers for improved rendering
Or the work by Jarabo et al. on propagation of light field edits.
However, these works focus on how to build up the correspondences to do these kind of edits, and work with light fields of a particular object, as opposed to light fields of a whole scene.
It is important to note that all this works propose editing tools for light fields, but they mostly do not pay special attention to the editing workflow or the interaction paradigm used.

## Slide 20
(More closely) Related Work
Lytro Filters
Lightfield Iris
[Lytro 2013]
[Vertical Horizon 2014]
There is an increasing need for editing this new content
Notes: Also related work are two commercial tools that are currently available and enable some modifications to a light field.
Both Lytro and Vertical Horizon presented tools for light field manipulation, but they both enable only global modifications of the light field based on pre-sets.
(The company Lytro presented some filters that can be applied on their light fields, but they are global filters that are applied by just selecting one predetermined filter or another.
Another company, Vertical Horizon, presented an app called Lightfield Iris for light field editing. But again, it enables only global modifications of the light field based on pre-sets.)

## Slide 21
There is a need for editing and manipulating this new content
Our goal: Explore users’ preferences when navigating & editing a light field
2D → 4D
→ Analyze light field editing interaction paradigms
, , …
?
Notes: What we do in this paper, and let me recover our goal here, is take the first steps towards tools in the spirit of the ones we have for 2D images, but for light fields, going beyond global pre-sets and filters.
And we do this by formalizing a number of interaction paradigms and analyzing them through various user studies.

## Slide 22: Interaction Paradigms
Two main paradigms:
  Multiview [Zhang02, Wang05, Shum04]
Notes: Once the problem is defined, looking at the literature we distill and formalize the two main interaction paradigms.
The first paradigm we call multiview, and is the most common in existing work on non-automatic light field editing.
(These paradigms are defined based on previous literature, on the different works which proposed some editing tools for the light field, like the ones we mentioned before.)

## Slide 23: Interaction Paradigms - Multiview
Source: lytro.com
Notes: In multiview, users navigate between the views of the light field to specify correspondences that locate their edits in space.
Essentially, multiview uses parallax to convey disparity, as done here.

## Slide 24: Interaction Paradigms
Two main paradigms:
  Multiview [Zhang02, Wang05, Shum04]
  Focus [Isaksen02, Davis12]
Notes: The second paradigm we call “Focus”.

## Slide 25: Interaction Paradigms - Focus
Source: T. Georgiev
Notes: And uses defocus blur as a cue to convey depth.
In focus, the light field is shown with a shallow depth of field to show the active depth where the editing can be done.

## Slide 26: Interaction Paradigms
Two main paradigms
  Multiview [Zhang02, Wang05, Shum04]
  → Parallax
  Focus [Isaksen02, Davis12]
  → Defocus blur
(based on two depth cues):
Notes: So basically both paradigms differ on that they rely on different depth cues to allow users visualize the disparity (or depth) in the light field.
Multiview relies on parallax, while focus relies on defocus blur.
We will show now how edits are done in each of the two.

## Slide 27: Interaction Paradigms - Multiview
view 1
view 2
view k
Notes: In Multiview the user first selects one view of the light field, and draws a stroke.
I will show you this both on the diagram and on the actual interface, part of which is shown on your right.
This stroke can be anywhere along that red line drawn.
To fix its actual position, the user needs to shift to another view, and adjust the depth of the stroke based on the observed parallax.
When satisified, the user fixes the position of the stroke, which can then be correctly observed on all other views.

## Slide 28: Interaction Paradigms - Focus
view 1
view 2
view k
Notes: In focus, the user works with the central view of the light field.
And again, I will be showing you the procedure both on the diagram and on the actual interface, shown on your right.
While before we first drew the stroke and then adjusted depth, in focus it is the other way around.
The user first adjusts the depth at which the stroke will be, by shifting the in-focus plane.
Once this in-focus plane is correctly positioned, the user draws a stroke.
This stroke is propagated to the rest of the views of the light field.

## Slide 29: Position in depth - Multiview
So…
how do people edit light fields?
Notes: And now, with all this background, let’s ask ourselves,
How do people edit light fields?

## Slide 30: Our user studies
Baseline experiment
  - Users preferences on interfaces
  - Synthetic light fields
Experiment with real light fields
  - Workflows on realistic edits
  - Captured light fields
Notes: In order to answer this question, we performed two experiments …(click)
The first one is a controlled baseline experiment, where we focus on finding users preferences when editing LF, (click) and we use synthetic light fields (click). We use the conclussions of this first experiment to feed the second one (click)
Where we focus on users workflows in real world edits, (click) using captured light fields (click).

## Slide 31
Task-based guided experiments
  Users perform a specific edit on a given light field
  Objective & subjective data is gathered
Our user studies – Characteristics
Notes: Both our user studies are designed as task-based experiments, where users are asked to perform specific edits into the given light field, given certain time; and where we gather objective and subjective data.

## Slide 32
Depth information plugged into both paradigms (F, MV)
  4 interfaces (F, MV, F+D, MV+D)
  Might not be always useful (e.g. imperfect depth, not editing on surfaces)
  Similar to 3D editing
Our user studies – Characteristics
Notes: Since light fields can be used to reconstruc depth from a scene, we also include this depth information into the two paradigms explained before, (click) whose combination gives 4 interfaces.
(click) we evaluate both with and without depth to evaluate users preferences, since depth don’t neccesarily need to be useful.
(click) note that using depth information transforms LF editing is similar to typical 3D modeling.

## Slide 33
Our user studies – Editing with Depth
VIDEO
Notes: Here is an example, where the user is asked to paint in the wall using MV+D. With this combination, this task simply requires drawing, since the depth positioning is done by just snapping the edits into the depth at the pixel.

## Slide 34
Point-based editing operations
  Most common editing tools
    Color brush, dodge/burn, clone…
  Building block for non-local tools
    Selection, coarse edit propagation, magic wand…
Our user studies – Characteristics
Notes: Finally, in our experiments we focus on point-based editing operations. We do that for two reasons:
First; many common operations is 2D editing software (e.g. PS) are based on this type of tools, such as brushes, dodge & burn, clone…
And second; this point-based interaction is the building block for non-local tools, such as selection, or edit propagation, where some point based interaction is required.

## Slide 35: Our user studies
Baseline experiment
  - Users preferences on interfaces
  - Synthetic light fields
Experiment with real light fields
  - Workflows on realistic edits
  - Captured light fields

## Slide 36
5 directed tasks in fixed order
Experiment 1 – Procedure
Notes: … We asked the users to perform 5 directed tasks, with different challenges such as:
(click) drawing in a planar surface,
(click) on a curved one,
(click) handling occlusions,
(click) editing view-dependent effects such as glossy reflections,
(click) and editing in free-space, that is, non on top of a surface.

## Slide 37
Experiment 1 – Procedure
5 directed tasks in fixed order
4 interfaces (F, FD, M, MD) in random order
Ground truth depth
Notes: Each of these tasks are performed in blocks for each interface (both F and MV, using and not using depth information), with the interfaces in random order. Note that we explore both using and not using depth, since depth might be not allways useful, or may not be available.
(click) Since we use synthetic light fields, we have perfect depth …
(click) and we gather both objective and subjective data.
Here we will explain the main findings of the experiment, and refer to the paper for details on the analysis and numerical results.

## Slide 38
  Task dependent
  Focus offers more sense of control, Multiview better for navigation
  Users prefer switching between interfaces
Hybrid Interface
Experiment 1 – Findings
Notes: The first main finding is that the preference for a given interface paradigm, is very tasks dependent.
In fact, the users reported their preference for switching between both paradigms, so they can get the best of each of them.

## Slide 39
    Depth info is not always useful
  Handling occlusions is challenging with depth alone
Depth Selection Tool
Experiment 1 – Findings
Notes: The second main finding is that, depending on the type of edit, depth is not always useful. In example, for editing on free space. Additionally, we found that depth alone is not enough to handle efficiently occlusions; thus, based on users suggestions, we incorporate a depth tool selection.

## Slide 40: Depth Selection tool
Select
Depth
Notes: This depth tool works as follows; first, the user selects the specific depth he wants to edit.

## Slide 41: Depth Selection tool
Selected
Masked Out
Edit on
selected areas
Notes: This creates a mask, based on depth… (click) that allows editing on the selected area, while masking out the unselected area.

## Slide 42: Depth Selection tool
Allows handling
occlussions
Notes: This allows handing occlusions pretty easily, as can be seen, where the sable edit has not been propagated to the computer.

## Slide 43: Our user studies
Baseline experiment
  - Users preferences on interfaces
  - Synthetic light fields
Experiment with real light fields
  - Workflows on realistic edits
  - Captured light fields
Hybrid Interface
Depth Selection tool
Notes: Based on the findings of the first experiment, we incorporate the proposed improvements in order to develop the new experiment.

## Slide 44: Experiment 2 – Procedure
10 directed tasks; random order
Hybrid interface
Reconstructed depth info available
  What impact does imperfect depth have?
Notes: We asked the users to perform 10 directed tasks, performed in random order (click).
We give the users complete freedom wrt interface, tools used, or using or not depth.
Additonally, here We use reconstructed depth. This allows us to study the effect that imperfect depth has on editing.
And, again, we gather objective and subjective data.

## Slide 45: Experiment 2 – Tasks
Notes: The 10 tasks of the experiment are done over 8 different light fields (click),
obtained from different sources, and with depth reconstructed with different algorithms

## Slide 46: Experiment 2 – Tasks
Handling occlusions
Notes: … handling occlussions (click)…

## Slide 47: Experiment 2 – Tasks
Handling occlusions
Occluder
Notes: … such as the shown here, where the users have to edit the wall, which is occluded by the tree.

## Slide 48: Experiment 2 – Tasks
Editing in free space
Notes: Edit on free space… (click)

## Slide 49: Experiment 2 – Tasks
Editing planar surfaces
Notes: Editing planar surfaces…

## Slide 50: Experiment 2 – Tasks
Intricate geometries
Notes: Editing over intrincate geometries…

## Slide 51: Experiment 2 – Tasks
Editing curved surfaces
Notes: Or editing on curved surfaces….

## Slide 52: Experiment 2 – Analysis
Subjective Data
- Ratings in post-task questions
Notes: We performed the experiment with 10 subjects, and collected and analyzed several data (click)
Including subjective data in the form of rating (click) and rankings for post tasks and post-experiment questions.

## Slide 53: Experiment 2 – Analysis
Subjective Data
- Ratings in post-task questions
- Ratings & rankings in final questions

## Slide 54: Experiment 2 – Analysis
Objective Data
Times of use of the different features and tools → workflows

## Slide 55: Experiment 2 – Analysis
Objective Data
Times of use of the different features and tools → workflows
Full analysis in the paper
and supplementary material
Notes: And objective data in the form of workflows (click). We refer to the paper and supplemental material for details on the data and analysis, and here we summarize the main conclussions of our study.

## Slide 56
A usable interface that allows performing common edits on a light field
Conclusions
Notes: After an analysis of this data, we found the following conclussions (click):
First of all, we found that the users are capable of performing common edits on light fields, and they found both the editing experience and the obtained results satisfactory.

## Slide 57: Editing results
Notes: In fact, we asked to perform more complex, open edits into new light fields, and got very compelling results; showing that we are able to perform complex photographic editing, without losing the capabilities of light fields….

## Slide 58
Users leverage the extra angular information in the 4D light field
Conclusions
Notes: We also found that users leverage the extra information in the light field to perform complex edits (click)

## Slide 59
Occlusions and complex geometries can be handled with the Depth Selection tool
  Utility of Depth Selection: 4.6/5
  Freq. of use Depth Selection: 4.7/5
  1: not at all – 5 very
Conclusions
Notes: Users also reported that the depth selection tool was very useful in order to handle occlusions, more than typical color selection tools.
Remember that occlusions could not be handled before in the first experiment

## Slide 60: Sample editing session
Notes: Here is an example where the depth picker is extensively used to avoid editing on unintended zones.

## Slide 61
Depth inaccuracies do not significantly affect editing
  Effect of depth inaccuracies in editing: 2.2/5
  Noticing inaccuracies in depth info: 2.2/5
  1: none – 5 a lot
Conclusions
Notes: Surprisingly, we found that depth inaccuracies do not affect much editing; we believe that this might be due to the type of inacuracies, and the nature of the edits.

## Slide 62
A LF Edit Interface would benefit from the easy navigation of multiview and the degree of control of focus
Conclusions
Notes: And our last conclusion is that we found that an ideal LFEI would need to combine the easy navigation given with MV, with the degree of control given by paradigms that make explicit the depth of edition, such as focus.

## Slide 63: Thanks!
Anonymous Reviewers
Participants of the experiments
P. Moosebrugger, S. López, J. I. Echevarría, C. A. Aliaga, R. Buisan, J. Marco, P. Hernando, L. Serra, C. K. Liang
LF and 3D models owners
Projects Verve, Golem, TAMA, Tropic, Intel Corp, Adobe, NVIDIA
Notes: And that’s all…

## Slide 64: Thanks!
Interface, Code & Data online:
http://giga.cps.unizar.es/~ajarabo/pubs/lfeiSIG14/
Notes: Finally, we have made our interface, source code and datasets available online; we hope that this will serve as a good starting point to develop future LF editing tools.
Thanks for your attention.

## Slide 65: Interfaces - Multiview

## Slide 66: Interfaces - Focus