## Slide 1: Zero-Phase Phasor Fields for Non-Line-of-Sight Imaging
Pablo Luesia-Lahoz, Talha Sultan, Forrest B. Peterson, Andreas Velten, Diego Gutierrez, Adolfo Muñoz
International Conference on Computational Photography 2025
Toronto, Canada, July 21-23

## Slide 2: Introduction
Notes: This is a common NLOS setup, and our target is to image this dragon around a corner

## Slide 3: NLOS Imaging applications
Driving safety
Rescue operations
Medical imaging
[7] Maeda, T., Satat, G., Swedish, T., Sinha, L., & Raskar, R. (2019). Recent advances in imaging around corners. arXiv preprint arXiv:1910.05613.
Figures adapted from previous work [7]

## Slide 4: Introduction
14h 54’ 55''
Dataset from Lindell et al. 2019
Hidden scene
Imaged dragon
Correct depth
2’ 1''
Notes: Previous NLOS have promising results
But struggles estimating depth precisely, requiring a lot of time
Our ZPPF estimates high depth precision, in efficient time

## Slide 5: Introduction
14h 54’ 55''
Dataset from Lindell et al. 2019
Ours error in depth
Error in depth
Correct depth
2’ 1''
Notes: Previous NLOS have promising results
But struggles estimating depth precisely, requiring a lot of time
Our ZPPF estimates high depth precision, in efficient time

## Slide 6: Non-Line-of-Sight (NLOS) Imaging
Hidden scene
Occluder
Relay wall
NLOS principle:
analyze the indirect illumination that reaches visible surfaces (relay wall).

## Slide 7: Non-Line-of-Sight (NLOS) Imaging
Hidden scene
Occluder
Relay wall

## Slide 8: Non-Line-of-Sight (NLOS) Imaging
Ultra-fast laser
Light emitted

## Slide 9: Non-Line-of-Sight (NLOS) Imaging
Light emitted

## Slide 10: Non-Line-of-Sight (NLOS) Imaging
Light emitted

## Slide 11: Non-Line-of-Sight (NLOS) Imaging
Ultra-fast camera
Captured signal
Transient imaging: picosecond resolution; captures light in motion
Confocal capture
Notes: Our ultrafast camera focus on same point.
So in this work we focus in confocal capture configuration.

## Slide 12: Non-Line-of-Sight (NLOS) Imaging
We capture a grid of points.

## Slide 13: Non-Line-of-Sight (NLOS) Imaging
y
x
Captured signal
y
x
time
We capture a grid of points.
How to employ this?

## Slide 14: Non-Line-of-Sight (NLOS) Imaging
y
x
[2] O’Toole, M., Lindell, D. B., & Wetzstein, G. (2018). Confocal non-line-of-sight imaging based on the light-cone transform. Nature, 555(7696), 338-341.
[3] Lindell, D. B., Wetzstein, G., & O'Toole, M. (2019). Wave-based non-line-of-sight imaging using fast fk migration. ACM Transactions on Graphics (ToG), 38(4), 1-13.
[5] Liu, X., Guillén, I., La Manna, M., Nam, J. H., Reza, S. A., Huu Le, T., ... & Velten, A. (2019). Non-line-of-sight imaging using phasor-field virtual wave optics. Nature, 572(7771), 620-623.
[4] Xin, S., Nousias, S., Kutulakos, K. N., Sankaranarayanan, A. C., Narasimhan, S. G., & Gkioulekas, I. (2019). A theory of fermat paths for non-line-of-sight shape reconstruction. In Proceedings of the IEEE/CVF conference on computer vision and pattern recognition (pp. 6800-6809).
NLOS methods
Filtered Back Projection [1]
Light Cone Transform [2]
F-K migration [3]
Fermat Paths [4]
Phasor Fields formulation [5]
Etc. Etc
[1] Velten, A., Willwacher, T., Gupta, O., Veeraraghavan, A., Bawendi, M. G., & Raskar, R. (2012). Recovering three-dimensional shape around a corner using ultrafast time-of-flight imaging. Nature communications, 3(1), 745.
Previous method struggle finding small depth variations in meter scale scenes

## Slide 15: Non-Line-of-Sight (NLOS) Imaging
y
x
NLOS methods
Filtered Back Projection [1]
Light Cone Transform [2]
F-K migration [3]
Fermat Paths [4]
Phasor Fields formulation [5]
Etc. Etc

## Slide 16: NLOS Imaging Methods
[2] O’Toole, M., Lindell, D. B., & Wetzstein, G. (2018). Confocal non-line-of-sight imaging based on the light-cone transform. Nature, 555(7696), 338-341.
[3] Lindell, D. B., Wetzstein, G., & O'Toole, M. (2019). Wave-based non-line-of-sight imaging using fast fk migration. ACM Transactions on Graphics (ToG), 38(4), 1-13.
[5] Liu, X., Guillén, I., La Manna, M., Nam, J. H., Reza, S. A., Huu Le, T., ... & Velten, A. (2019). Non-line-of-sight imaging using phasor-field virtual wave optics. Nature, 572(7771), 620-623.
[4] Xin, S., Nousias, S., Kutulakos, K. N., Sankaranarayanan, A. C., Narasimhan, S. G., & Gkioulekas, I. (2019). A theory of fermat paths for non-line-of-sight shape reconstruction. In Proceedings of the IEEE/CVF conference on computer vision and pattern recognition (pp. 6800-6809).
NLOS methods
Filtered Back Projection [1]
Light Cone Transform [2]
F-K migration [3]
Fermat Paths [4]
Phasor Fields formulation [5]
Etc. Etc
[1] Velten, A., Willwacher, T., Gupta, O., Veeraraghavan, A., Bawendi, M. G., & Raskar, R. (2012). Recovering three-dimensional shape around a corner using ultrafast time-of-flight imaging. Nature communications, 3(1), 745.

## Slide 17: NLOS Imaging Methods
NLOS methods
Filtered Back Projection [1]
Light Cone Transform [2]
F-K migration [3]
Fermat Paths [4]
Phasor Fields formulation [5]
Etc. Etc

## Slide 18: Background: The Phasor Fields Formulation
Relay wall
y
Hidden scene
Lateral view of the setup

## Slide 19: Background: The Phasor Fields Formulation
Illumination and capture points

## Slide 20: Background: The Phasor Fields Formulation
Captured signal
Notes: Lets take the captured signal of this point

## Slide 21: Background: The Phasor Fields Formulation
Captured signal
Virtual Gaussian wave packet
*
Virtual phasor
Notes: Virtual Gaaussian wave packet modulate the capture
Result is a Virtual phasor

## Slide 22: The Phasor Fields Formulation
Captured signal
Virtual Gaussian wave packet
*
Virtual phasor
Virtual phasor:
Scene as lit with the Gaussian wave packet
Notes: Virtual Gaaussian wave packet modulate the capture

## Slide 23: Background: The Phasor Fields Formulation
Captured signal
…
…
…
A phasor field
Notes: We can apply the same modulation to the capture of all points
Result into a field of phasors or a phasor field
The phasor field is used to image instead

## Slide 24: Background: The Phasor Fields Formulation
…
Image point
The imaged point is a phasor:
amplitude + phase
Propagation of the phasor field
Notes: We image a point
Imaging with phasors equivalent to wavefront propagation in line of sight
The imaged point also yields a phasor: amplitude and phase

## Slide 25: Background: The Phasor Fields Formulation
…
Image plane
[6] Liu, X., Bauer, S., & Velten, A. (2020). Phasor field diffraction based reconstruction for fast non-line-of-sight imaging systems. Nature communications, 11(1), 1645.
Image point
Efficient Phasor Fields implementations exist to propagate plane to plane [6]
Notes: More efficient implementations exists for plane to plane propagation

## Slide 26: Finding geometry with Phasor Fields
Bunny position
Amplitude
0
The closest plane to the surface
Notes: We reconstruct continum depth to form line
Look at amplitude
Bunny position corresponds to maximum
To identify the amplitude:
  PF employ efficient plane implementation
  Distribute them in the space
  Select the maximum
  THE CLOSEST PLANE TO THE SURFACE

## Slide 27: Finding geometry with Phasor Fields
Bunny position
Amplitude
0
Plane away from hidden surface
gap
gap
More resolution = more planes = more execution time
Notes: There is a plane
There is a gap in bunny position and plane
Increase the depth resolution requires more planes that increases the execution time

## Slide 28: Our Zero-Phase Phasor Fields
Bunny position
Amplitude
0
0
We employ the phase, discarded by previous methods
Phase
Notes: We present now our Zero-Phase Phasor Fields
Remember we are looking at the imaged amplitude across line in depth
Imaged line contains phase and amplitude
Phase was discarded
Ours employ phase back

## Slide 29: Our Zero-Phase Phasor Fields
0
Phase
0
Bunny position
Imaged plane
The imaged phase crosses to zero at the true surface positions
Notes: We now focus on phase
In this part specifically
Here we have phase evolution, imaged plane, and bunny position
We can observe here the key observation of the paper:
  PHASE CROSS TO ZERO

## Slide 30: Our Zero-Phase Phasor Fields
0
Imaged plane
We know the phase at imaged plane
Corrected depth
Bunny position
Notes: Face known at imaged plane
  Look at green line crossing orange
We can correct its positioning using that

## Slide 31: Summarizing methods
Image planes, then select maximum in depth
Increase depth precision by increasing imaged planes
Phasor Fields (PF)
Dense PF
Our Zero-Phase Phasor Fields
Phase correction
Image planes, selects maximum, and corrects depth
Notes: To recap, we have phasor fields.
  With this relay wall and imaged planes
Images planes and select máximum
A straight forward solution to increase depth precision is dense PF

## Slide 32: Summarizing methods
Image planes, then select maximum in depth
Increase depth precision by increasing imaged planes
Phasor Fields (PF)
Dense PF
Our Zero-Phase Phasor Fields
Phase correction
Image planes, selects maximum, and corrects depth
Notes: To recap, we have phasor fields.
  With this relay wall and imaged planes
Images planes and select máximum
A straight forward solution to increase depth precision is dense PF

## Slide 33: Results

## Slide 34: Results
Planar patch simulation [7] under micrometer displacement
Our ZPPF depth
PF depth
0
1
-1
0.996
1
Ground truth
Patch at 1m
Patch depth | Distance to 1m between ZPPF depths
1 m | 0.0µm
z
x
[7] Royo, D., García, J., Muñoz, A., & Jarabo, A. (2022). Non-line-of-sight transient rendering. Computers & Graphics, 107, 84-92.

## Slide 35: Results
Planar patch simulation [7] under micrometer displacement
0
1
-1
0.996
1
Patch at 1m + 500 µm
Patch depth | Distance to 1m between ZPPF depths
1 m | 0.0
1m + 500µm | 492.60µm
z
x
Our ZPPF depth
PF depth
Ground truth
[7] Royo, D., García, J., Muñoz, A., & Jarabo, A. (2022). Non-line-of-sight transient rendering. Computers & Graphics, 107, 84-92.

## Slide 36: Results
Planar patch simulation [7] under micrometer displacement
Our ZPPF depth
PF depth
0
1
-1
0.996
1
Ground truth
Patch at 1m + 250 µm
Patch depth | Distance to 1m between ZPPF depths
1 m | 0.0µm
1m + 500µm | 492.60µm
1m + 250µm | 246.21µm
z
x
[7] Royo, D., García, J., Muñoz, A., & Jarabo, A. (2022). Non-line-of-sight transient rendering. Computers & Graphics, 107, 84-92.

## Slide 37: Results
Planar patch simulation [7] under micrometer displacement
Our ZPPF depth
PF depth
0
1
-1
0.996
1
Ground truth
Patch at 1m + 125 µm
Patch depth | Distance to 1m between ZPPF depths
1 m | 0.0µm
1m + 500µm | 492.60µm
1m + 250µm | 246.21µm
1m + 125µm | 123.23µm
z
x
[7] Royo, D., García, J., Muñoz, A., & Jarabo, A. (2022). Non-line-of-sight transient rendering. Computers & Graphics, 107, 84-92.

## Slide 38: Results
Planar patch simulation [7] under micrometer displacement
Our ZPPF depth
PF depth
0
1
-1
0.996
1
Ground truth
Patch at 1m + 125 µm
Patch depth | Distance to 1m between ZPPF depths
1 m | 0.0µm
1m + 500µm | 492.60µm
1m + 250µm | 246.21µm
1m + 125µm | 123.23µm
z
x
Correctly estimate depth variations
[7] Royo, D., García, J., Muñoz, A., & Jarabo, A. (2022). Non-line-of-sight transient rendering. Computers & Graphics, 107, 84-92.

## Slide 39: Results
Two planar patch simulation [7], and one under small offset of micrometer
[7] Royo, D., García, J., Muñoz, A., & Jarabo, A. (2022). Non-line-of-sight transient rendering. Computers & Graphics, 107, 84-92.

## Slide 40: Results
Two planar patch simulation [7], and one under small offset of micrometer
Our ZPPF depth
PF depth
Ground truth
0
1
-1
0.996
1
No offset
z
x
[7] Royo, D., García, J., Muñoz, A., & Jarabo, A. (2022). Non-line-of-sight transient rendering. Computers & Graphics, 107, 84-92.

## Slide 41: Results
Two planar patch simulation [7], and one under small offset of micrometer
Our ZPPF depth
PF depth
Ground truth
0
1
-1
0.996
1
No offset
z
x
500 µm offset
0
1
-1
0.996
1
x
[7] Royo, D., García, J., Muñoz, A., & Jarabo, A. (2022). Non-line-of-sight transient rendering. Computers & Graphics, 107, 84-92.

## Slide 42: Results
Two planar patch simulation [7], and one under small offset of micrometer
Our ZPPF depth
PF depth
Ground truth
0
1
-1
0.996
1
No offset
z
x
0
1
-1
0.996
1
250 µm offset
x
[7] Royo, D., García, J., Muñoz, A., & Jarabo, A. (2022). Non-line-of-sight transient rendering. Computers & Graphics, 107, 84-92.

## Slide 43: Results
Two planar patch simulation [7], and one under small offset of micrometer
Our ZPPF depth
PF depth
Ground truth
0
1
-1
0.996
1
No offset
z
x
0
1
-1
0.996
1
125 µm offset
x
[7] Royo, D., García, J., Muñoz, A., & Jarabo, A. (2022). Non-line-of-sight transient rendering. Computers & Graphics, 107, 84-92.

## Slide 44: Results
Two planar patch simulation [7], and one under small offset of micrometer
Our ZPPF depth
PF depth
Ground truth
0
1
-1
0.996
1
No offset
z
x
0
1
-1
0.996
1
125 µm offset
x
[7] Royo, D., García, J., Muñoz, A., & Jarabo, A. (2022). Non-line-of-sight transient rendering. Computers & Graphics, 107, 84-92.
Notes: This is very useful for depth estimation

## Slide 45: Results – simulated plane at 1 m
PF depth
Our ZPPF depth
Ground truth
0
1
-1
0.996
1
Top view of simulated plane
Depth
x
Displace half of the plane 500 µm
Notes: We simulated a plane at 1 meter
PF place the plane here, showing this gap of around 5 mm
Ours reduce this gap
We now split the plane, and displace it 500 micrometers

## Slide 46: Results – simulated plane at 1 m
PF depth
Our ZPPF depth
Ground truth
0
1
-1
0.996
1
Top view of simulated plane
Depth
x
Displace half of the plane 500 µm
Displace half of the plane 125 µm
Our method recover the micrometers depth variations
Notes: We observe a step in gt
PF again uses same plane
Ours reduce the gap, furthermore, it shows the same step
Our results shows we can see this even in the 125 micrometer case

## Slide 47: Results – simulated plane at 1 m
PF depth
Our ZPPF depth
Ground truth
0
1
-1
0.996
1
Top view of simulated plane
Depth
x
Displace half of the plane 125 µm
Notes: This extreme case
We place this horizontal line to highlight our depth also shows this variation

## Slide 48: Results – Depth recovery of real dataset
Hidden scene
Dense PF depth
PF depth diff.
Ours depth diff.
Depth (m)
0.95
1.15
Diff
(m)
0.0
0.16
9h 28' 54''
2’ 4''
2’ 10''
Data from publicly available dataset [3]
[3] Lindell, D. B., Wetzstein, G., & O'Toole, M. (2019). Wave-based non-line-of-sight imaging using fast fk migration. ACM Transactions on Graphics (ToG), 38(4), 1-13.

## Slide 49: Results
Imaging real captures using a publicly available dataset [3]
Hidden scene
Dense PF depth
PF depth diff.
Ours depth diff.
Depth (m)
0.95
1.15
Diff
(m)
0.0
0.16
9h 28' 54''
2’ 4''
2’ 10''

## Slide 50: Results
Imaging real captures using a publicly available dataset [3]
[3] Lindell, D. B., Wetzstein, G., & O'Toole, M. (2019). Wave-based non-line-of-sight imaging using fast fk migration. ACM Transactions on Graphics (ToG), 38(4), 1-13.
Hidden scene
Dense PF depth
PF depth diff.
Ours depth diff.
Depth (m)
1.28
1.40
Diff.
(m)
0.0
0.16
13h 54’ 55''
2’ 1''
2’ 10''

## Slide 51: Results – decreasing signal to noise ratio
180 mins
Depth (m)
1.28
1.40
10 mins
1 min
15 sec
PF amplitude
Ours depth
Notes: Publicly available dataset, in lowering exposure time – reduce SNR
Upper Amplitude
Amplitude dragón shape degrades with low snr
Our Depth is consistent

## Slide 52: Results
Imaging real captures using a publicly available dataset [3], varying exposure time (different SNR)
[3] Lindell, D. B., Wetzstein, G., & O'Toole, M. (2019). Wave-based non-line-of-sight imaging using fast fk migration. ACM Transactions on Graphics (ToG), 38(4), 1-13.
Amplitude
ZPPF depth
ZPPF diff.
Depth (m)
1.28
1.40
Diff.
(m)
0.0
0.1
180 mins of capture time

## Slide 53: Results
Imaging real captures using a publicly available dataset [3], varying exposure time (different SNR)
[3] Lindell, D. B., Wetzstein, G., & O'Toole, M. (2019). Wave-based non-line-of-sight imaging using fast fk migration. ACM Transactions on Graphics (ToG), 38(4), 1-13.
Amplitude
ZPPF depth
ZPPF diff.
Depth (m)
1.28
1.40
Diff.
(m)
0.0
0.1
30 mins of capture time

## Slide 54: Results
Imaging real captures using a publicly available dataset [3], varying exposure time (different SNR)
[3] Lindell, D. B., Wetzstein, G., & O'Toole, M. (2019). Wave-based non-line-of-sight imaging using fast fk migration. ACM Transactions on Graphics (ToG), 38(4), 1-13.
Amplitude
ZPPF depth
ZPPF diff.
Depth (m)
1.28
1.40
Diff.
(m)
0.0
0.1
10 mins of capture time

## Slide 55: Results
Imaging real captures using a publicly available dataset [3], varying exposure time (different SNR)
[3] Lindell, D. B., Wetzstein, G., & O'Toole, M. (2019). Wave-based non-line-of-sight imaging using fast fk migration. ACM Transactions on Graphics (ToG), 38(4), 1-13.
Amplitude
ZPPF depth
ZPPF diff.
Depth (m)
1.28
1.40
Diff.
(m)
0.0
0.1
1 mins of capture time

## Slide 56: Results
Imaging real captures using a publicly available dataset [3], varying exposure time (different SNR)
[3] Lindell, D. B., Wetzstein, G., & O'Toole, M. (2019). Wave-based non-line-of-sight imaging using fast fk migration. ACM Transactions on Graphics (ToG), 38(4), 1-13.
Amplitude
ZPPF depth
ZPPF diff.
Depth (m)
1.28
1.40
Diff.
(m)
0.0
0.1
15 sec of capture time

## Slide 57: Conclusions
Phasor Fields (PF)
Dense PF
Our Zero-Phase Phasor Fields
Efficient in time
Efficient memory consumption
Low depth precision
Efficient in time
Efficient memory consumption
High depth precision
Inefficient in time
Inefficient memory consumption
High depth precision
Notes: To recap, we have phasor fields.
  With this relay wall and imaged planes
Images planes and select máximum
A straight forward solution to increase depth precision is dense PF

## Slide 58: Conclusions
We develop a method that efficiently estimates depth.
Depth recovery using phase is robust to noise.
Future work and limitations:
  Derive for non-confocal.
  Phase correction works when the imaged plane is close enough.
  Small mismatches occur, possibly due to near-field diffraction.

## Slide 59: Zero-Phase Phasor Fields for Non-Line-of-Sight Imaging
Pablo Luesia-Lahoz, Talha Sultan, Forrest B. Peterson, Andreas Velten, Diego Gutierrez, Adolfo Muñoz
International Conference on Computational Photography 2025
Toronto, Canada, July 21-23
9h 28' 54''
2’ 4''
2’ 10''